## Slide 1: Verilog

## Slide 2: 4-Value Logic
Four values:
  0, 1, x, z.
    x: unknown value
    z: high impedance
and | 0 | 1 | x | z
0 | 0 | 0 | 0 | 0
1 | 0 | 1 | x | x
x | 0 | x | x | x
z | 0 | x | x | x
or | 0 | 1 | x | z
0 | 0 | 1 | x | x
1 | 1 | 1 | 1 | 1
x | x | 1 | x | x
z | x | 1 | x | x
input | not
0 | 1
1 | 0
x | x
z | x

## Slide 3: Vectors
  output [0:3] D;
  wire [7:0] SUM;
  indexing:
    D[3]
  slicing:
    SUM[5:2]

## Slide 4: Decoder
//HDL Example 4-1
//----------------------------------------
//Gate-level description of a 2-to-4-line decoder
//Figure 4-19
module decoder_gl (A,B,E,D);
input A,B,E;
output [0:3] D;
wire Anot,Bnot,Enot;
not
n1 (Anot,A),
n2 (Bnot,B),
n3 (Enot,E);
nand
n4 (D[0],Anot,Bnot,Enot),
n5 (D[1],Anot,B,Enot),
n6 (D[2],A,Bnot,Enot),
n7 (D[3],A,B,Enot);
endmodule
  Gate-level description
  nands and nots are grouped.

## Slide 5: Buffers
  gateName (output, input, control);
bufif1 (OUT, A, control);
notif0 (Y, B, enable);

## Slide 6: Multiplexer
module muxtri (A, B, select, OUT);
input A, B, select;
output OUT;
tri OUT;
bufif1 (OUT, A, select);
bufif0 (OUT, B, select);
endmodule;
tri:
  a net which has the capability of being driven by several drivers.
types of nets:
  wire, tri, supply1, supply0, wand, wor.
OUT
Correct?