## Slide 1: Verilog

## Slide 2: Hierarchical Design
  4-bit adder in terms of full-adders
  Full-adders in terms of half-adders
  Half-adders in terms of gates.
//HDL Example 4-2
//-----------------------------------------------
//Gate-level hierarchical description of 4-bit adder
// Description of half adder (see Fig 4-5b)
module halfadder (S,C,x,y);
input x,y;
output S,C;
//Instantiate primitive gates
xor (S,x,y);
and (C,x,y);
endmodule

## Slide 3: Hierarchical Design
//Description of full adder (see Fig 4-8)
module fulladder (S,C,x,y,z);
input x,y,z;
output S,C;
wire S1,D1,D2; //Outputs of first XOR and two AND gates
//Instantiate the halfadder
halfadder HA1 (S1,D1,x,y),
HA2 (S,D2,S1,z);
or g1(C,D2,D1);
endmodule
D1
S1
D2

## Slide 4: Hierarchical Design
//Description of 4-bit adder (see Fig 4-9)
module _4bit_adder (S,C4,A,B,C0);
input [3:0] A,B;
input C0;
output [3:0] S;
output C4;
wire C1,C2,C3; //Intermediate carries
//Instantiate the fulladder
fulladder FA0 (S[0],C1,A[0],B[0],C0),
FA1 (S[1],C2,A[1],B[1],C1),
FA2 (S[2],C3,A[2],B[2],C2),
FA3 (S[3],C4,A[3],B[3],C3);
endmodule

## Slide 5: Dataflow Description
Using some operators and signal assignments
  concat appends two operands and makes a larger one.
operator | Operation
+ | Binary addition
- | Binary subtraction
& | Bitwise and
¦ | Bitwise or
^ | Bitwise xor
~ | Bitwise not
== | Equality
> | Greater
< | Less
{ } | Concatenation
?: | Conditional

## Slide 6: Decoder
//HDL Example 4-3
//----------------------------------------------
//Dataflow description of a 2-to-4-line decoder
//See Fig.4-19
module decoder_df (A,B,E,D);
input A,B,E;
output [0:3] D;
assign D[0] = ~(~A & ~B & ~E),
D[1] = ~(~A & B & ~E),
D[2] = ~(A & ~B & ~E),
D[3] = ~(A & B & ~E);
endmodule
  continuous assignment:
    assigns a value to a net (wire, output).

## Slide 7: MUX
assign Y = (A & S) | (B & ~S);
//HDL Example 4-6
//----------------------------------------
//Dataflow description of 2-to-1-line multiplexer
module mux2x1_df (A,B,select,OUT);
input A,B,select;
output OUT;
assign OUT = select ? A : B;
endmodule

## Slide 8: 4-Bit Adder
//HDL Example 4-4
//----------------------------------------
//Dataflow description of 4-bit adder
module binary_adder (A,B,Cin,SUM,Cout);
input [3:0] A,B;
input Cin;
output [3:0] SUM;
output Cout;
assign {Cout,SUM} = A + B + Cin;
endmodule
  + can be used to add binary numbers.
  Cout and SUM are concatenated.

## Slide 9: 4-Bit Comparator
//HDL Example 4-5
//-----------------------------------
//Dataflow description of a 4-bit comparator.
module magcomp (A,B,ALTB,AGTB,AEQB);
input [3:0] A,B;
output ALTB,AGTB,AEQB;
assign ALTB = (A < B),
AGTB = (A > B),
AEQB = (A == B);
endmodule
  Comparison operators can be used to compare n-bit numbers.

## Slide 10: Behavioral Modeling
//HDL Example 4-7
//---------------------------------
//Behavioral description of 2-to-1-line multiplexer
module mux2x1_bh(A,B,select,OUT);
input A,B,select;
output OUT;
reg OUT;
always @ (select or A or B)
if (select == 1) OUT = A;
else OUT = B;
endmodule
  Uses always and an expression:
    Change in any variable after @  runs again
    Statements within always: sequential
      e.g. if else
    Output of always construct must be reg.
      A reg net keeps its value until a new value is assigned

## Slide 11: 4-1 MUX (Behavioral)
//HDL Example 4-8
//-------------------------------------
//Behavioral description of 4-to-1- line multiplexer
//Describes the function table of Fig. 4-25(b).
module mux4x1_bh (i0,i1,i2,i3,select,y);
input i0,i1,i2,i3;
input [1:0] select;
output y;
reg y;
always @ (i0 or i1 or i2 or i3 or select)
case (select)
2'b00: y = i0;
2'b01: y = i1;
2'b10: y = i2;
2'b11: y = i3;
endcase
endmodule
  For combinational circuits, all variables to be read must be used in sensitivity list.

## Slide 12: Simulation and Synthesis
Synthesis
  Automatic design.
  Software program takes design description and tries to find the circuit
کامپايل
شبيه سازي
ورود طرح
ويرايش
سنتز
شبيه سازي
ويرايش
کامپايل
اجرا
برنامه نويسي
ويرايش

## Slide 13: Testbench
initial
begin
A = 1; B = 0;
#10 A = 0;
#20 A = 1; B = 1;
end
Testbench:
  Applies inputs and is used to see the outputs.
  Uses initial to drive the values.
    runs once.
  always runs many times

## Slide 14: Testbench
  001 is added to D seven times with 10 time units in between.
initial
begin
D = 3’b000;
repeat (7)
#10 D = D + 3’b001;
end

## Slide 15: Testbench Structure
  Testbench items:
    test module name
    reg and wire declarations
    instantiation of circuit under test
    initial/always statement
    outputs display
  No input/output ports:
    Signals are applied through local regs.
    Outputs to be displayed are declared as wires.

## Slide 16: Testbench
  You can see waveforms
  Values can be displayed by Verilog system tasks:
    $display: displays variable value once (with newline)
      $display (format, argument list);
    $write: as $display without newline,
    $monitor: displays any variable that is changed during simulation.
    $time: shows simulation time.
    $finish: finishes simulation.
$display (“%d %b %b”, C, A, B);
$display (“time = %0d A = %b B = %b”, $time, A, B)

## Slide 17: Testbench: Example
//HDL Example 4-9
//----------------------------
//Stimulus for mux2x1_df.
module testmux;
reg TA,TB,TS; //inputs for mux
wire Y; //output from mux
mux2x1_df mx (TA,TB,TS,Y);//instantiate mux
initial
begin
TS = 1; TA = 0; TB = 1;
#10 TA = 1; TB = 0;
#10 TS = 0;
#10 TA = 0; TB = 1;
end
initial
$monitor("select = %b A = %b B = %b OUT = %b time = %0d",
TS, TA, TB, Y, $time);
endmodule
//Dataflow description of 2-to-1-line multiplexer
//from Example 4-6
module mux2x1_df (A,B,select,OUT);
input A,B,select;
output OUT;
assign OUT = select ? A : B;
endmodule
  Testbench items:
    test module name,
    reg and wire declarations,
    instantiation of circuit under test,
    initial/always statement,
    outputs display,

## Slide 18: Testbench
  %0d is better for time because %d reserves 10 positions.
  MUX inputs: reg,
  MUX output: wire.

## Slide 19: Testbench: Example 2

## Slide 20: Testbench: Example2
//HDL Example 4-10
//------------------------------------------
//Gate-level description of circuit of Fig. 4-2
module analysis (A,B,C,F1,F2);
input A,B,C;
output F1,F2;
wire T1,T2,T3,F2not,E1,E2,E3;
or g1 (T1,A,B,C);
and g2 (T2,A,B,C);
and g3 (E1,A,B);
and g4 (E2,A,C);
and g5 (E3,B,C);
or g6 (F2,E1,E2,E3);
not g7 (F2not,F2);
and g8 (T3,T1,F2not);
or g9 (F1,T2,T3);
endmodule
//Stimulus to analyze the circuit
module test_circuit;
reg [2:0]D;
wire F1,F2;
analysis fig42(D[2],D[1],D[0],F1,F2);
initial
begin
D = 3'b000;
repeat(7)
#10 D = D + 1'b1;
end
initial
$monitor ("ABC = %b F1 = %b F2 =%b ",D, F1, F2);
endmodule
Simulation Log:
ABC = 000 F1 = 0 F2 =0
ABC = 001 F1 = 1 F2 =0
ABC = 010 F1 = 1 F2 =0
ABC = 011 F1 = 0 F2 =1
ABC = 100 F1 = 1 F2 =0
ABC = 101 F1 = 0 F2 =1
ABC = 110 F1 = 0 F2 =1
ABC = 111 F1 = 1 F2 =1